## Slide 1: N-bit Full Adder
Design and implementation of n bit full Adder

## Slide 2: Introduction
An N-bit adder performs addition of two N-bit binary numbers.
Implemented using multiple full adders connected in series (Ripple-Carry Adder).
Verilog generate and genvar allow automatic hardware replication for scalable design.

## Slide 3: Why use genvar?
Reduces repetitive code.
Easy to scale from 4-bit → 8-bit → 32-bit by changing a single parameter.
Ensures cleaner and modular RTL design.
Commonly used in datapath units, ALUs, and processor design.

## Slide 4: Block Diagram
Full Adder
[0]
Full Adder
[1]
Full Adder
[2]
Full Adder
[3]
Full Adder
[N-1]
A[0]
A[1]
A[2]
B[0]
B[1]
B[2]
A[3]
B[3]
A[N-1]
B[N-1]
S[0]
S[1]
S[2]
S[3]
S[N-1]
C[0]
C[1]
C[2]
C[3]
C[N-1]
Cin

## Slide 5: Verilog code for n bit adder module
module fulladder(sum,cout,a,b,c);
input a,b,c;
output sum,cout;
assign sum=a^b^c;
assign cout=(a&b)|((a^b)&c);
endmodule
module n_bitadder #(parameter N=4)(sum,cout,a,b,cin);
input [N-1:0] a,b;
input cin;
output [N-1:0] sum;
output cout;
wire [N-1:0]c;
assign c[0]=cin;
genvar i;
generate
for(i=0;i<N;i=i+1) begin
fulladder fa(sum[i],c[i+1],a[i],b[i],c[i]);
end
endgenerate
assign cout=c[N];
endmodule
Full Adder:
N_bit Full Adder:

## Slide 6: Testbench for N bit Adder
`include "n_bitadder.v"
module top;
parameter N=4;
reg [N-1:0]a,b;
reg cin;
wire [N-1:0] sum,c;
wire cout;
n_bitadder nadd (sum,cout,a,b,cin);
initial begin
repeat(10)begin
a=$random();
b=$random();
cin=$random();
#10;
$monitor ("time=%0t| a-> %b,b-> %b,cin->%b | sum->%b ,cout-> %b|",$time,a,b,cin,sum,cout);
end
end
endmodule

## Slide 7: Working Principle
Each full adder computes: sum[i] = A[i] ⊕ B[i] ⊕ carry_in
Carry propagates to the next stage: carry_out → next carry_in
Final carry-out is cout.
Delay increases with number of bits (Ripple effect).

## Slide 8: Features:
Parameterized hardware (N can be any size).
Reusable and scalable design.
Synthesizable for FPGA/ASIC.
Suitable for datapath blocks in CPUs.

## Slide 9: Applications:
ALU design
Microprocessor datapaths
Signal processing units
Arithmetic circuits in FPGA designs

## Slide 10
Thank you
By
Mr. AKASH K